## Slide 1: Beyond Just Beam Errors Direction-Dependent Calibration Challenges Far from the Phase Center
Stefanie Brackenhoff
Kapteyn Astronomical Institute
Advisors:
Prof. dr. Léon Koopmans (Kapteyn)
Prof. dr. ir. Alle-Jan van der Veen (TU Delft)
Dr. André Offringa (ASTRON/Kapteyn)
Dr. Maaijke Mevius (ASTRON)

## Slide 2: Motivation
Beam errors are a challenge for high contrast projects
  Issue for 21-cm cosmology
    Limiting NenuFAR results (Munshi et al., 2024)
    Need for uv-excision in LOFAR data (~19 % data loss)

## Slide 3: Motivation
Beam errors are a challenge for high contrast projects
  Limits results for 21-cm cosmology
  Signal can stay buried under sidelobes of bright sources
Issue pressing for
Bright sources
A-team sources
High beam variability
(nulls & sidelobes)
Signal not detectable
High contrast study

## Slide 4: Motivation
Beam errors are a challenge for high contrast projects
  Limits results for 21-cm cosmology
  Signal can stay buried under sidelobes of bright sources
Issue pressing for
Bright sources
A-team sources
High beam variability
(nulls & sidelobes)
Signal not detectable
High contrast study
I will be talking about the HBA

## Slide 5: The structure of the beam

## Slide 6: Beams in 4D
2x spatial
Temporal
Spectral

## Slide 7: Beams in 4D
CS002HBA0 – CS101HBA0 1.1km
2x spatial
Temporal
Spectral

## Slide 8: Beams in 4D
Voltage-beam (dB)
*array factor only: assumes omnidirectional elements at the lowest level
Phase center
CS002HBA0 – CS101HBA0 1.1km
2x spatial
Temporal
Spectral

## Slide 9: Beams in 4D
π
-π
0
0
60
Time (min)
2x spatial
Temporal
Spectral
CS002HBA0 – CS101HBA0 1.1km

## Slide 10: Current EoR calibration

## Slide 11: Calibration
Sky and beam models
Predict in a direction
Sky model with beam on baseline i,j

## Slide 12: Calibration
Sky and beam models
Predict in a direction
Find gains that minimize the difference between model and data
Sky model with beam on baseline i,j

## Slide 13: Calibration
Sky and beam models
Predict in a direction
Find gains that minimize the difference between model and data
Direction-dependent
gains
Sky model with beam on baseline i,j

## Slide 14: Calibration
Sky and beam models
Predict in a direction
Find gains that minimize the difference between model and data
Direction-dependent
gains
directions
Sky model with beam on baseline i,j

## Slide 15: Calibration
Sky and beam models
Predict in a direction
Find gains that minimize the difference between model and data
Measured visibility
Direction-dependent
gains
directions
Sky model with beam on baseline i,j

## Slide 16: Calibration
Sky and beam models
Predict in a direction
Find gains that minimize the difference between model and data
Measured visibility
Direction-dependent
gains
DDECal: smoothing kernel
SAGECal: polynomial basis
directions
Sky model with beam on baseline i,j

## Slide 17: Beam unmodelled
= not calibrating in this direction anymore
We predict without the beam (computationally cheaper)
➡ Large errors near the nulls

## Slide 18: Beam unmodelled
This is not effective in the far field!

## Slide 19: Far-field spectral smoothing with a perfect beam model

## Slide 20: Perfect beam model
Prediction of Cas A
Residual
Even if we can fully model the beam, we need to be careful about smoothing the solutions
Predict Cas A + NCP
Add thermal noise
Calibrate DD ➡ gains
Take noiseless prediction of Cas A (left) and subtract with gains

## Slide 21: Perfect beam model
Prediction of Cas A
Residual
Even if we can fully model the beam, we need to be careful about smoothing the solutions

## Slide 22: Perfect beam model
cartoon
Forward prediction very weak at null

## Slide 23: Perfect beam model
cartoon
Weight with forward prediction
Forward prediction very weak at null

## Slide 24: Perfect beam model
Weight with forward prediction

## Slide 25: Perfect beam model
Reweighted smoothing
Residual
Even if we can fully model the beam, we need to be careful about smoothing the solutions

## Slide 26: Perfect beam model
Reweighted smoothing
Residual
Future work: test this with beam errors

## Slide 27: Beam errors
cartoons

## Slide 28: Primary beam errors

## Slide 29: LOFAR beams

## Slide 30: LOFAR beams

## Slide 31: Missing tiles (implemented)
Spatial Change
Altered beam
Original beam

## Slide 32: Missing dipoles (not implemented)
Spatial Change
Altered beam
Original beam

## Slide 33: Dipole gain variation (not implemented)
Spatial Change
Altered beam
Original beam

## Slide 34: Future Work

## Slide 35: Altered spectral smoothness constraint
Far field sources must allow non-smoothness in their regularized solutions
  DDECal: reweight the smoothing kernel
  SAGECal: different basis near nulls
2x spatial
Temporal
Spectral
Easy to implement
Fits naturally in existing pipeline
Expertise exists
Only works for high S/N ratio
More degrees of freedom needed

## Slide 36: Fitting the station beam
Allow for variations of the elements within a station to fit the station beam directly
  Slowly varying direction-dependent gains result from this
2x spatial
Temporal
Spectral
Based on physics
Theoretically able to describe all directions (also fainter sources)
May remove need for (high number of) solution intervals and calibration directions
Entirely new technique (may not work)
Requires many degrees of freedom to calibrate station

## Slide 37: Summary & Future work

## Slide 38: Issues with beams in calibration
We cannot model nulls/rapidly varying lobes far from the phase center well in our current calibration strategy
  Changes within a solution interval
  Changes on spectral scales << smoothness scale
  Changes on spatial scales smaller than a cluster
For bright clusters, we can alter the regularization
For the full problem, we would need to fit the station beam

## Slide 39: Supplements

## Slide 40: Beams in calibration
Can not model all station beams fully
  In-situ spatiotemporal variations, mutual coupling, manufacturing variations etc.
Both Sagecal and DDECal contain:
  Dipole beam (EM simulated model)
  Array factor of all dipoles
  Tile flagging
  Option to calibrate on a station level
Neither have:
  Full array EM simulation (not feasible)
  Discrete analogue beamformer
  Intra-tile flagging
  Option to calibrate on a lower level
Dipole
Tile array factor
Station array factor

## Slide 41
The issue with modelling the beam
A small error can move a null / grating lobe significantly
Analogue tile beamformer
Voltage-beam amplitude ratio (dB)
Voltage-beam phase difference (rad)

## Slide 42: Smoothing tests DDEcal
Ook met beam error

## Slide 43: Better model!
Temperature drift [ref]
Elements breaking
Discrete steering
Higher order effects (mutual coupling, manufactoring variation etc)

## Slide 44: Displacing nulls
A small error can move a null significantly
  A null moving has 2 effects
    A null in data but not in model
    A null in model but not in data
A real beam will always be more smooth than a model beam
  Real array less regular  helps with data nulls
  Worry on model side
Exact model placement
σ=1 cm placement errors
Linear dipole array

## Slide 45: Reweighted smoothing
Beam error

## Slide 46: Reweighted smoothing
Perfect beam match

## Slide 47: Reweighted smoothing
Perfect beam match